Latice-Boltzmann Report

1 Introduction

In this assignment we were asked to optimise an implementation of the Lattice-Boltmann algorithm for simulating fluids according to the Boltzmann equation. First it was required to perform a series of serial optimisations to the code to minimise its run time on a single processor core, then to implement OpenMP techniques to allow the code to be run on multiple processes of the same node to allow for parallelisation. The first thing I did was select the compiler and compiler flags that I would use to produce the lowest run times. I found that by using ICC 7.1.0 with the flags -Ofast and AVX, these flags tell the compiler to maximise the optimisations it performs on the code and to generate SIMD instructions based on the CPU architecture respectively. Using these compiler options on the originally provided code produces run times on square grids of size 128x128, 256x256 and 1024x1024 of around 25.2s, 202.8s, and respectively.

2. Serial Optimisations
2.1 Loop Fusion

The first serial optimisation I performed was to perform a loop fusion by combining the functioning of the rebound() and collision() functions into one function. This means that we reduce the number of times the program needs to iterate over the grid, thus reducing the number of arithmetic and memory operations performed and resulting in a speed up. I also realised that it was possible to merge av_velocity() into the same function as the local_density, u_x and u_y calculations were just repeated from the collision() function. This meant that I could have the newly created large function return the av_vels calculation, which in tern I had the timestep() function return to be assigned to the the av_vels[tt] array. I found that trying to merge the propagate function into the same function resulted in the run times being increased, so I held off on merging it as well until I was making the functions vectorise. These improvements resulted in the run time of the program acting on a 128x128 grid being reduce to