Latice-Boltzmann Report

1 Introduction

In this assignment we were asked to optimise an implementation of the Lattice-Boltmann algorithm for simulating fluids according to the Boltzmann equation. First it was required to perform a series of serial optimisations to the code to minimise its run time on a single processor core, then to implement OpenMP techniques to allow the code to be run on multiple processes of the same node to allow for parallelisation. The first thing I did was select the compiler and compiler flags that I would use to produce the lowest run times. I found that by using ICC 7.1.0 with the flags -Ofast and AVX, these flags tell the compiler to maximise the optimisations it performs on the code and to generate SIMD instructions based on the CPU architecture respectively. Using these compiler options on the originally provided code produces run times on square grids of size 128x128, 256x256 and 1024x1024 of around 25.2s, 202.8s, and 714.7s respectively.

2. Serial Optimisations
2.1 Loop Fusion

The first serial optimisation I performed was to perform a loop fusion by combining the functioning of the rebound() and collision() functions into one function. This means that we reduce the number of times the program needs to iterate over the grid, thus reducing the number of arithmetic and memory operations performed and resulting in a speed up. I also realised that it was possible to merge av_velocity() into the same function as the local_density, u_x and u_y calculations were just repeated from the collision() function. This meant that I could have the newly created large function return the av_vels calculation, which in tern I had the timestep() function return to be assigned to the the av_vels[tt] array. I found that trying to merge the propagate function into the same function resulted in the run times being increased, so I held off on merging it as well until I was making the functions vectorise. These improvements resulted in the run time of the program acting on a 128x128 grid being reduce to 19.6s.

2.2. Pointer Swapping

In the original code, the entire grid is copied from the cells grid, into the tmp_cells grid and then back to the cells grid for each iteration of timestep, it quickly became clear that this was unessary and that only one copy operation was requred per timestep, which would obviously cut down on the number of memory operations performed and thus increasing performance. To do this all nine speeds for each cells (the loop acts on one cell per iteration) are transferred into temporary variables, which are then used for the rest of the calculations so they only need to be copied into tmp_cells once. At the end of the loop this obviously leaves the current grid arrangement in the tmp_cells grid, so I had to edit the tt timestep loop so that it stepped by 2 each time and that for av_vels[tt] is trasfered the grid from cells to tmp_cells and for av_vels[tt+1] it copied the cells back from tmp_cells to cells.

2.3 Arithmentic Optimisations

A simpler, but important, optimisation was to improve the arithmetic within the loops to make optimisation easier for the compiler, this was mostly done within the calculations of the d_equ[x] variables and was done but removing the costing division operations, by inverting the c_sq variable from 1/3 to 3 and then replacing the division operation with a multiplication and using the updated c_sq whilst replacing the constants of 2 with their inverse of 0.5, which is mathematically the same equation however using far faster operations. I also during this optimisation replaced constants such as 0.5 * c_sq * c_sq which are calculated multiple times with variables calculated at the start of the function, so that they only need to be calculated once per iteration and then reused.

2.4 Vectorisation

To make sure the compiler did the maximum amount of optimisation possible, I first went through all the variables in the code and set them to const if they were not going to be changed at any point, this helps the compiler to produce faster code. Also in the parameters to functions I set as many variables as possible to have the restrict keyword in front of them, this tells the compiler that there will be no overlap between variables, which is important between the cells and tmp_cells arrays. A significant change I made in the code was to change the data layout from an Array of Structures configuration to a Structure of Arrays configuration. The original AoS format is one where you have a struct containing each of the 9 speeds, and then you store an array of these struts, one for each cell, this is optimal for serial code as it is better for data locality, when you access speeds[0] you also bring speeds[1]-[15] into the cache due the 64-byte cache size.The SoA structure on the other hand consists of a structure which contains an array for each 9 speeds. Applying this change initially slows the code down by around 6 seconds on the 128x128 grid, however once the compiler starts vectorising the code efficiently the speed gain is far greater than this. To help the compiler further, I used memory techniques including swapping malloc() function calls for _mm_malloc() calls instead, which returns the data aligned to a requested boundary, in my case 64 bytes to match the cache size. Also at the start of each function call to the main calculation function I added _assume_alligned() statements which tells the compiler the pointer it is describing are aligned, which allows the compiler to optimise further. Finally, I added #pragma omp simd outside the start of each loop which explicitly tells the compiler to vectorise these loops if possible.

3 OpenMP Optimisation
3.1 Having successfully performed serial optimisations including getting the compiler to vectorise the code, I moved onto to using the OpenMP interface to allow the code to run on multiple threads.